## Slide 1: Public Input Meeting Sandy Pond Road Complete Streets Improvements
Town of Ayer
Department of Public Works
September 13th,
2023

## Slide 2: What is a Complete Street?
MassDOT: “A Complete Street is one that provides safe and accessible options for all travel modes – walking, biking, transit and vehicles – for all ages and disabilities”.

## Slide 3: MassDOT Complete Streets Funding Program
2016: MassDOT launched Complete Streets funding program
Up to $500,000 available to participating communities every four years

## Slide 4: Sandy Pond Road (Snake Hill Road to Westford Road)
50’ right-of-way, 4,800’ long (0.9 miles)
30’ wide road (13’ wide travel lanes, 1’ – 2’ wide shoulders)
No sidewalks, curbing, bike lanes, or ADA compliant crossings

## Slide 5: Sandy Pond Road – Typical Section

## Slide 6: Sandy Pond Road at Snake Hill Road

## Slide 7: Sandy Pond Road at Easy Street

## Slide 8: Sandy Pond Road at Patriot Way

## Slide 9: Sandy Pond Road at Mountain Laurel Road

## Slide 10: Sandy Pond Road at Westford Rd & Willow Rd

## Slide 11: Sandy Pond Road – Complete Streets Study (Snake Hill Road to Westford Road)
The DPW requested funding from Town Meeting for the Study after receiving numerous requests to complete the project
Ayer DPW contracted with Consultant to provide complete street conceptual design & cost estimate
Two concept options studied

## Slide 12: Concept ‘A’ – Shared Use Path
11’ wide travel lanes with 2’ wide shoulders
8’ to 10’ wide “shared-use” path (south side of roadway)
Mill & overlay of roadway + pavement markings
Drainage upgrades and granite curbing
Flashing Beacons (Snake Hill Road and Mount Laurel Road)
Preliminary Estimate: $1,800,000

## Slide 13: Concept ‘B’ – Sidewalk & Bike Lanes
11’ wide travel lanes with 5’ wide bike lanes (each side)
5’ wide sidewalk (south side of roadway)
Mill & overlay of roadway and new pavement markings
Drainage upgrades and granite curbing
Flashing Beacons (Snake Hill Road and Mount Laurel Road)
Preliminary Estimate: $1,700,000

## Slide 14
Concept ‘B’ (Sidewalk & Bike Lanes) is preferred
Cost can be reduced significantly through value engineering
Recommend phasing construction to maximize use of funding
Consultant’s Conclusion

## Slide 15
Recommended Construction Phasing

## Slide 16
Sandy Pond Road Phase 1
Snake Hill Road to Patriot Way (2024/2025)

## Slide 17
August 2023 – Ayer DPW awarded grant for $500,000 to construct Phase 1 (Snake Hill Road to Patriot Way).
Ayer DPW to provide design, permitting, and construction management of Phase 1 work
Sandy Pond Road Phase 1
Snake Hill Road to Patriot Way (2024/2025)

## Slide 18: Sandy Pond Road at Snake Hill Road Conceptual Plan

## Slide 19: Sandy Pond Road at Easy Street Conceptual Plan

## Slide 20: Sandy Pond Road at Patriot Way Conceptual Plan

## Slide 21
Sandy Pond Road Phase 2 (Date TBD)
Patriot Way to Westford Road

## Slide 22
Phase 2 can be value-engineered close to $500,000
DPW investigating other funding alternatives to expedite Phase 2 construction
DPW would wait until 2027 to apply for Phase 2 Construction through MassDOT Complete Streets Funding
Sandy Pond Road Phase 2 (Date TBD)
Patriot Way to Westford Road

## Slide 23
Implement public input into Phase 1 design & planning
Design Phase 1 work (construction plans & specifications)
Place Phase 1 project out for bid and award contract
Contact direct abutters once a construction schedule has been set for Phase 1
Continue to seek available funding for Phase 2 construction
Next Steps

## Slide 24: Thank You
Dan Van Schalkwyk, p.e., Director of public works
Matt herNON, P.E., TOWN ENGINEER